Digital Design Lab #7: Decoders and Multiplexers in HDL
Charlie Coleman
Lab Partner: Luke Taylor
2016 October 20

Objective: The objective of this lab was to gain experience using Hardware Description Language while designing the seven segment decoder, a functions using a decoder, and multiplexers.

Design:
1A) In part one, we were to redesign the seven segment decoder, but use HDL instead of a schematic. The functions were the same as before.

Code:
entity lab7project is
    Port ( A : in STD_LOGIC;
        B : in STD_LOGIC;
        C : in STD_LOGIC;
        D : in STD_LOGIC;
        Sa : out STD_LOGIC;
        Sb : out STD_LOGIC;
        Sc : out STD_LOGIC;
        Sd : out STD_LOGIC;
        Se : out STD_LOGIC;
        Sf : out STD_LOGIC;
        Sg : out STD_LOGIC);
end lab7project;

architecture Behavioral of lab7project is

begin
Sa <= ((not A) and (not B) and (not C) and D) or ((not A) and B and (not C) and (not D)) or (A and B and (not C) and D) or (A and (not B) and C and D);
Sb <= ((not A) and B and (not C) and D) or (A and B and (not D)) or (A and C and D) or (B and C and (not D));
Sc <= ((not A) and (not B) and C and (not D)) or (A and B and (not D)) or (A and B and C);
Sd <= ((not A) and B and (not C) and (not D)) or (B and C and D) or (A and (not B) and C and (not D)) or ((not B) and (not C) and D);
Se <= ((not A) and D) or ((not A) and B and (not C)) or ((not B) and (not C) and D);
Sf <= ((not A) and (not B) and D) or ((not A) and (not B) and C) or ((not A) and C and D) or (A and B and (not C) and D);
Sg <= ((not A) and (not B) and (not C)) or ((not A) and B and C and D) or (A and B and (not C) and (not D));

end Behavioral;
2A) In part 2A, we were to design a 4:16 decoder using HDL. The decoder acted as a normal decoder would, activating the decimal equivalent line to the input values. The functions for each output were found via Karnaugh maps.

Code:
entity decoder4_16 is
    Port ( A : in STD_LOGIC;
        B : in STD_LOGIC;
        C : in STD_LOGIC;
        D : in STD_LOGIC;
        y : out STD_LOGIC_vector(15 downto 0));

end decoder4_16;

architecture Behavioral of decoder4_16 is

begin
y(0) <= not A and not B and not C and not D;
y(1) <= not A and not B and not C and D;
y(2) <= not A and not B and C and not D;
y(3) <= not A and not B and C and D;
y(4) <= not A and B and not C and not D;
y(5) <= not A and B and not C and D;
y(6) <= not A and B and C and not D;
y(7) <= not A and B and C and D;
y(8) <= A and not B and not C and not D;
y(9) <= A and not B and not C and D;
y(10) <= A and not B and C and not D;
y(11) <= A and not B and C and D;
y(12) <= A and B and not C and not D;
y(13) <= A and B and not C and D;
y(14) <= A and B and C and not D;
y(15) <= A and B and C and D;

end Behavioral;
2C) For part 2C, the 4:16 decoder used in part 2A was to be used to implement 8 functions. The decoder was used as a component in the code, and the functions were implemented using OR gates with decoder outputs.

Code:
entity functions8 is
    Port ( A : in STD_LOGIC;
        B : in STD_LOGIC;
        C : in STD_LOGIC;
        D : in STD_LOGIC;
        f0 : out STD_LOGIC;
        f1 : out STD_LOGIC;
        f2 : out STD_LOGIC;
        f3 : out STD_LOGIC;
        f4 : out STD_LOGIC;
        f5 : out STD_LOGIC;
        f6 : out STD_LOGIC;
        f7 : out STD_LOGIC);
end functions8;

architecture Behavioral of functions8 is
COMPONENT decoder4_16
PORT(
A : IN std_logic;
B : IN std_logic;
C : IN std_logic;
D : IN std_logic;
y : OUT std_logic_vector(15 downto 0)
);
END COMPONENT;
signal ysignal: std_logic_vector(15 downto 0);
begin
Inst_decoder4_16: decoder4_16 PORT MAP(
A => A,
B => B,
C => C,
D => D,
y => ysignal
);

f0 <= ysignal(0) or ysignal(14) or ysignal(15);
f1 <= ysignal(1) or ysignal(13) or ysignal(15);
f2 <= ysignal(2) or ysignal(12) or ysignal(15);
f3 <= ysignal(3) or ysignal(11) or ysignal(15);
f4 <= ysignal(4) or ysignal(10) or ysignal(15);
f5 <= ysignal(5) or ysignal(9) or ysignal(15);
f6 <= ysignal(6) or ysignal(8) or ysignal(15);
f7 <= ysignal(7) or ysignal(15);
end Behavioral;
3A) For part 3, a quad 4:1 multiplexer was to be implemented. A quad 4:1 MUX takes 4 groups of 4 inputs and 2 select lines, and outputs the group of inputs who's decimal value is the same as the select line's decimal value. This code used when and else statements.

Code:
entity multiplexer4_1 is
    Port ( s0 : in STD_LOGIC;
        s1 : in STD_LOGIC;
        a0 : in STD_LOGIC;
        a1 : in STD_LOGIC;
        a2 : in STD_LOGIC;
        a3 : in STD_LOGIC;
        b0 : in STD_LOGIC;
        b1 : in STD_LOGIC;
        b2 : in STD_LOGIC;
        b3 : in STD_LOGIC;
        c0 : in STD_LOGIC;
        c1 : in STD_LOGIC;
        c2 : in STD_LOGIC;
        c3 : in STD_LOGIC;
        d0 : in STD_LOGIC;
        d1 : in STD_LOGIC;
        d2 : in STD_LOGIC;
        d3 : in STD_LOGIC;
        y0 : out STD_LOGIC;
        y1 : out STD_LOGIC;
        y2 : out STD_LOGIC;
        y3 : out STD_LOGIC);
end multiplexer4_1;

architecture Behavioral of multiplexer4_1 is

begin
y0 <= a0 when (s1 = '0' and s0 = '0') else
b0 when (s1 = '0' and s0 = '1') else
c0 when (s1 = '1' and s0 = '0') else
d0 when (s1 = '1' and s0 = '1');
y1 <= a1 when (s1 = '0' and s0 = '0') else
b1 when (s1 = '0' and s0 = '1') else
c1 when (s1 = '1' and s0 = '0') else
d1 when (s1 = '1' and s0 = '1');
y2 <= a2 when (s1 = '0' and s0 = '0') else
b2 when (s1 = '0' and s0 = '1') else
c2 when (s1 = '1' and s0 = '0') else
d2 when (s1 = '1' and s0 = '1');
y3 <= a3 when (s1 = '0' and s0 = '0') else
b3 when (s1 = '0' and s0 = '1') else
c3 when (s1 = '1' and s0 = '0') else
d3 when (s1 = '1' and s0 = '1');
end Behavioral;

Procedure: To begin, we used the seven segment decoder lab and rewrote the design using VHDL. The Xilinx software was used to do this, and the code is shown above. To do this, we created a new source from project and used the VHDL Module setting. We set the 4 inputs A, B, C, and D to the in direction, and the outputs OUTPUTS set to out direction. This created the entity above and we simply added in the equations under architecture. We synthesized and tested the design and printed the result. We then coded a 4-16 decoder using VHDL. This was done by setting the four inputs A, B, C, and D to the in direction under the VHDL Module, and the outputs Y­0-Y15 to the out direction. We then coded the decoder into the architecture setting and compiled and tested. We then used the decoder as a component to implement the functions

This was done by creating a new VHDL source and setting the inputs A, B, C, and D to in, and the outputs f1-f7 to out. The decoder was made into a component by clicking the View VHDL Insantitation Template. It was used in the new source by copying the component section and pasting it to the new one under architecture, and the instant section into the behavioral section. This function was then compiled simulated and printed. Lastly, we created a multiplexer circuit. This was done by writing a VHDL code to implement a 4-1 mux that multiplexes 4 bits at a time. This was done by connecting the A0 B0 C0 and D­0 to the Y0 output. The same was done for Y1, Y2, and Y3. The mux was then compiled and simulated for the following inputs;
S(1:0) = 00 A(3:0) = 0000 B(3:0) = 0001 C(3:0) = 0010 D(3:0) = 0011
S(1:0) = 00 A(3:0) = 0110 B(3:0) = 0001 C(3:0) = 0010 D(3:0) = 0011
S(1:0) = 00 A(3:0) = 1100 B(3:0) = 0001 C(3:0) = 0010 D(3:0) = 0011
S(1:0) = 01 A(3:0) = 0001 B(3:0) = 0101 C(3:0) = 0010 D(3:0) = 0011
S(1:0) = 01 A(3:0) = 0001 B(3:0) = 1101 C(3:0) = 0010 D(3:0) = 0011
S(1:0) = 01 A(3:0) = 0001 B(3:0) = 1111 C(3:0) = 0010 D(3:0) = 0011
S(1:0) = 10 A(3:0) = 0001 B(3:0) = 0001 C(3:0) = 0100 D(3:0) = 0011
S(1:0) = 10 A(3:0) = 0001 B(3:0) = 0001 C(3:0) = 0110 D(3:0) = 0011
S(1:0) = 10 A(3:0) = 0001 B(3:0) = 0001 C(3:0) = 1001 D(3:0) = 0011
S(1:0) = 11 A(3:0) = 0001 B(3:0) = 0001 C(3:0) = 0010 D(3:0) = 1010
S(1:0) = 11 A(3:0) = 0001 B(3:0) = 0001 C(3:0) = 0010 D(3:0) = 1100
S(1:0) = 11 A(3:0) = 0001 B(3:0) = 0001 C(3:0) = 0010 D(3:0) = 0011

Data: See attached Xilinx simulation results.

Data Analysis: For each of our Xilinx designs, the simulated results matched the expected results. For the seven segment decoder and the decoder functions, we were able to test the program on the board, seeing that the results were as expected. The decoder was tested only using Xilinx, not put on the board. The truth table was checked for accuracy compared to the expected output of a decoder. For the MUX, the number of input lines was too large to test all possible combinations, so test vectors given in the lab were used and results were compared to expected output of a MUX. Each design was a success.

Conclusion: In this lab, we were to gain experience with HDL by implementing multiple different designs which we had previously done using schematics. Learning HDL is helpful because HDL is important for and makes some more advanced designs possible. Schematics can become very cluttered very quickly, and HDL code is often easier to troubleshoot and examine. Some challenges faced in this weeks lab was learning to use a previous code as a component instead of just copying the code, which was learned in lab. We also had some trouble using vectors.