Digital Design Prelab #8
Charlie Coleman
2016 October 27

1A)

D Flip Flop
entity DFlipFlop is
    Port ( D : in STD_LOGIC;
        CLK : in STD_LOGIC;
        Q : inout STD_LOGIC);
end DFlipFlop;

architecture Behavioral of DFlipFlop is

begin
ff : process(CLK, D)
begin
if(CLK = '1') then
Q <= D;
end if;
end process;

end Behavioral;

Edge Triggered D Flip Flop
entity EdgeTriggeredDFlipFlop is
    Port ( D : in STD_LOGIC;
        CLK : in STD_LOGIC;
        Q : inout STD_LOGIC);
end EdgeTriggeredDFlipFlop;

architecture Behavioral of EdgeTriggeredDFlipFlop is

COMPONENT DFlipFlop
PORT(
D : IN std_logic;
CLK : IN std_logic;
Q : INOUT std_logic
);
END COMPONENT;
signal Qhold : STD_LOGIC;
signal Qfinal: STD_LOGIC;
begin

DFlipFlop_1: DFlipFlop PORT MAP(
D => D,
CLK => "not"(CLK),
Q => Qhold
);
DFlipFlop_2: DFlipFlop PORT MAP(
D => Qhold,
CLK => CLK,
Q => Qfinal
);
Q <= Qfinal;

end Behavioral;

Four Bit Register
entity FourBitRegister is
    Port ( D1 : in STD_LOGIC;
        D2 : in STD_LOGIC;
        D3 : in STD_LOGIC;
        D4 : in STD_LOGIC;
        CLK : in STD_LOGIC;
        Q1 : out STD_LOGIC;
        Q2 : out STD_LOGIC;
        Q3 : out STD_LOGIC;
        Q4 : out STD_LOGIC);
end FourBitRegister;

architecture Behavioral of FourBitRegister is

COMPONENT EdgeTriggeredDFlipFlop
PORT(
D : IN std_logic;
CLK : IN std_logic;
Q : INOUT std_logic
);
END COMPONENT;
signal Q1temp : STD_LOGIC;
signal Q2temp : STD_LOGIC;
signal Q3temp : STD_LOGIC;
signal Q4temp : STD_LOGIC;
begin

ETDFlipFlop1: EdgeTriggeredDFlipFlop PORT MAP(
D => D1,
CLK => CLK,
Q => Q1temp
);
ETDFlipFlop2: EdgeTriggeredDFlipFlop PORT MAP (
D => D2,
CLK => CLK,
Q => Q2temp
);
ETDFlipFlop3: EdgeTriggeredDFlipFlop PORT MAP (
D => D3,
CLK => CLK,
Q => Q3temp
);
ETDFlipFlop4: EdgeTriggeredDFlipFlop PORT MAP (
D => D3,
CLK => CLK,
Q => Q4temp
);
Q1 <= Q1temp;
Q2 <= Q2temp;
Q3 <= Q3temp;
Q4 <= Q4temp;

end Behavioral;

2.A.a)
entity Decode2_4e is
    Port ( S0 : in STD_LOGIC;
        S1 : in STD_LOGIC;
        EN : in STD_LOGIC;
        Y0 : out STD_LOGIC;
        Y1 : out STD_LOGIC;
        Y2 : out STD_LOGIC;
        Y3 : out STD_LOGIC);
end Decode2_4e;

architecture Behavioral of Decode2_4e is

begin

Y0 <= not S1 and not S0 and EN;
Y1 <= not S1 and S0 and EN;
Y2 <= S1 and not S0 and EN;
Y3 <= S1 and S0 and EN;

end Behavioral;